Sno-Kone Machine Operation

Warning: Do not put your fingers or any object into the shaver body while the motor is running. Serious injury may occur.

Ice Requirements:    Cubes or pieces of block ice no larger than 3”-4”.  One 10# bag           of ice will make 20 sno-kones (1/2# of ice per sno-kone).

Syrup Requirements:  1 gallon of prepared syrup will make 128-1 ounce servings

Electrical Requirements:  120 volt electrical outlet.

Time Requirements:  Shaved ice melts quickly so prepare it shortly before serving unless refrigeration is available.

Instructions:

- Switch the motor on.  There are separate switches for the motor and the display lights.  The motor toggle switch is on the motor body.  The switch for the display light is located inside the case near the fluorescent light.

- Wait for the motor to come to full speed (a minute or so).

- Fill the gooseneck to within an inch of the top with ice cubes or block ice (no larger than 3” to 4”).  The larger the pieces, the better the snow.

- Push the pusher handle down against the ice in the gooseneck.  Apply firm and even pressure to make the best snow.    Practice will allow you to gauge when to stop pressing.  This allows the ice to resettle against the cutter head.  You may find that you need to relieve the pressure two or three times in a cycle.  Over pressing will stall the motor.  In this case, relieve the pressure and try again.  Too much pressure will result in snow that is course; too little pressure will make the snow mushy.

- Under normal operating conditions, the motor will become very warm.  A surface temperature of 150 degrees is normal.

Caution:

- Never allow foreign or metallic objects around the shaver area.  Blades can be damaged by foreign objects.

- Do not immerse the equipment in water.